## Slide 1
01
Autonomous
Human-Robot
Interaction
Real-Time Face Tracking & Ultrasonic Spatial Mapping with OhBot
Python
OpenCV
YuNet
OhBot
ATmega32U4
Core idea
A robotic head that sees faces, moves naturally, senses nearby objects, and shows its perception on a radar map.
Presented by: Sazzad Abdullah Mahbub Ul Islam Khan

## Slide 2
Project objective
What the system is built to do
02
Human detection
Detect faces using a camera and AI-based face detection.
Natural motion
Eyes handle small movements. The head moves when the face moves far from center.
Object awareness
Dual ultrasonic sensors detect nearby objects on the left and right side.
Recovery behavior
When the face is lost, the robot searches using ultrasonic direction cues.
Basic operating values
640 × 480
Camera resolution
30 FPS
Camera frame rate
250 cm
Ultrasonic threshold
2.5 s
Face lost timeout
8 frames
Position buffer

## Slide 3
System architecture
Camera and sonar are processed together in Python
03
USB
Camera
OpenCV
Frame Input
YuNet / Haar
Face Detection
Tracking
Controller
OhBot
Servos
Left + Right
HC-SR04
ATmega32U4
Microcontroller
Serial JSON
115200 baud
Output: live camera HUD + radar map + servo motion

## Slide 4
Face detection and tracking
How the robot decides where to look
04
Detect
face
Find center
Cx, Cy
Calculate
error
Smooth
movement
Move eyes
/head
Detector
Primary: YuNet
Fallback: Haar Cascade
Multi-face target: middle face
Control zones
Eye-zone margin: 20%
Center area: eye only
Outer area: head + eyes
Stability values
Head smoothing: 0.08
Eye smoothing: 0.20
Dead zone: 0.07
Design choice: eyes react faster, while the head stays smoother and less jerky.

## Slide 5
When the face is lost
Vision first, ultrasonic recovery second
05
No face
detected
Wait
2.5 seconds
Read left/right
ultrasonic
Turn toward
closest side
Decision logic
Left distance smaller → turn left
Right distance smaller → turn right
No object under threshold → return to center
Why this matters
The robot keeps a basic sense of direction even when the camera temporarily loses the person.
2.5 s
Lost timeout
< 250 cm
Object threshold
0.04
Head return smoothing

## Slide 6
06
LIVE DEMO
Walk in front of the robot. Watch it follow you.

## Slide 7
Hardware values and servo limits
Important values used by the program
07
Ultrasonic wiring
LEFT sensor
TRIG → Pin 9
ECHO → Pin 8
RIGHT sensor
TRIG → Pin 11
ECHO → Pin 10
Neutral positions
Head pan: 5.0
Head nod: 6.2
Eye pan: 5.0
Eye tilt: 5.0
Safe movement ranges
Head pan: 1.0 to 9.0
Head nod: 5.2 to 7.5
Eye pan: 1.0 to 9.0
Eye tilt: 3.5 to 7.0
COM13
Serial port
115200
Baud rate
250 cm
Object threshold

## Slide 8
Environmental scan and radar
The robot maps faces and objects during scanning
08
Radar view
Scan values
Pan range: 2.0 to 8.0
Scan positions: 11
Settling delay: 0.55 s
Radar values
Display size: 600 × 600 px
Range rings: 50, 100, 150, 200 cm
Green marker: face
Yellow marker: object
Duplicate handling
Nearby face detections are clustered if pan difference ≤ 2.0. This prevents one person from appearing as many people.

## Slide 9
Main improvements and conclusion
What the final code achieves
09
1. Serial communication fix
DTR/RTS enabled for ATmega32U4 native USB streaming.
2. Scan stability
Servo settling delay and frame-buffer flushing reduce scan jitter.
3. Mechanical compensation
Continuous nod hold prevents head sag from camera and sensor weight.
4. Cleaner radar
Detection clustering merges duplicate adjacent face sightings.
Final result
Computer vision + servo control + ultrasonic sensing + radar visualization
The OhBot can detect faces, track a target, sense nearby objects, recover after losing visual contact, and scan its surroundings.
Thank you